## Slide 1
AUTONOMOUS FLEET TESTBED
A CI/CD-Native Testing Framework
for Autonomous Robots
Enterprise release discipline, applied to robotics — plus an AI agentic test-and-heal loop
Mike · Release 1 · 2026

## Slide 2
THE PROBLEM
Robotics Lacks Software's Release Discipline
• Sim and real-world testing are separate, ad hoc efforts There's rarely one pipeline that proves a robot works in simulation and on hardware, before every release.
• Regressions get caught late On the bench, or in the field — not in a fast, cheap feedback loop measured in seconds.
• Test scenarios are static The same fixed suite runs release after release; nothing generates new scenarios to find new bugs.
• No systematic drift detection Without a rolling baseline, a robot that's slowly getting worse looks the same as one that isn't — until it fails.
autonomous-fleet-testbed

## Slide 3
THE SOLUTION
Proven Before Every Release
A local-first, CI/CD-native pipeline that proves a robot's software works — in simulation and on real hardware — before it ships. Two products, mutually reinforcing:
FLEET CI/CD PIPELINE FRAMEWORK
"How do you know your robot software
works before it touches hardware?"
• Robot-agnostic, open-source-ready
• Built on ROS2, Gazebo, Isaac Sim, GitHub Actions
• Lives in tools/ + .github/workflows/
AI AUTONOMOUS MISSION PLANNER
"How do you tell a fleet what to do —
and prove they can do it?"
• Scripted missions today, AI-driven next
• Generates the scenarios the pipeline tests
• Lives in src/nav_fleet/
The pipeline validates the planner. The planner generates the scenarios the pipeline tests.
autonomous-fleet-testbed

## Slide 4
SHIFT LEFT
Find 90% of Bugs Before CI Even Starts
x86 Bare Metal
~1 sec build
colcon build, Python unit tests
Gazebo Harmonic
throughput tier
Fast headless nav sim, seconds per run
Isaac Sim
fidelity tier
Photorealistic physics, perception-grade
Real Hardware
ground truth
Jetson Orin Nano + Waveshare UGV — Session 14/15
x86 bare metal finds 90% of bugs at ~1s build time vs. 23+ minutes in emulated CI — debug locally, commit to CI only when clean.
autonomous-fleet-testbed

## Slide 5
ARCHITECTURE
The 6-Stage CI/CD Pipeline
Stage 0
Requirements
Traceability
Stage 1
Code Quality
(ament lint)
Stage 2
arm64
Cross-Compile
Stage 3
Gazebo
Simulation
Stage 4
Isaac Sim
(fidelity)
Stage 5
Reports +
Dashboard
Stage 6
Real Robot Deploy
Sessions 14–15
• Every stage gates the next — a requirement with no test, or a lint failure, blocks the pipeline before it ever reaches sim.
autonomous-fleet-testbed

## Slide 6
ARCHITECTURE
Telemetry: One Schema, Every Backend
Gazebo
Harmonic
Isaac Sim
Real Robot
(Session 15)
ROS2 Jazzy + Nav2
(same test suite, sim_engine tag)
telemetry_logger.log_run()
SQLite
(single source of truth)
PDF Reports
Streamlit
Dashboard
Drift Detector
(rolling baseline)
Agentic Loop
(Session 13)

## Slide 7
DISCIPLINE
Requirements Traceability — a CI Gate, Not a Spreadsheet
Every requirement maps to a real, executing test. A requirement with no test fails the build.
ID
Requirement
Test
BR-01
Robot reaches goal within 0.15 m
test_navigation_succeeds
BR-02
Zero collisions per run
test_no_collision
BR-04
Odometry publishes ≥ 50 Hz
test_odom_message_schema
BR-07
Nav success rate ≥ 95% (rolling 20 runs)
test_drift_detected_above_threshold
SC-04 / SC-05
Lidar / camera publish ≥ 10 Hz
test_scan / test_camera_image_schema
BR-03
Recovery behavior (backup/spin)
no test yet — tracked as a real, open gap
autonomous-fleet-testbed · requirements/traceability.yaml

## Slide 8
DISCIPLINE
Drift Detection — Behavioral Regression, Not Just Pass/Fail
• Rolling baseline Every metric compared against the last 20 PASS runs, not a fixed absolute number.
• Sigma-threshold flagging A run more than 2σ from the historical mean gets flagged for investigation.
• Config as data Thresholds live in config/drift_config.yaml — never hardcoded in Python.
• Verified for real Seeded 9 realistic runs, injected one 10x position-error outlier — flagged at sigma = 122, everything else stayed clean.
baseline_monitor.py — real output
Baseline drift report — run 11
--------------------------------------------
FLAGGED mean_position_error sigma=122.0
OK mean_time_to_goal sigma=0.3
OK odom_hz_mean sigma=0.5
OK lidar_hz_mean sigma=0.0
OK camera_hz_mean sigma=0.5
--------------------------------------------
1 metric(s) flagged — investigate before release.
autonomous-fleet-testbed · tools/baseline_monitor.py

## Slide 9
THE DIFFERENTIATOR
Agentic Test-and-Heal Loop
1
Read Telemetry
Latest run + rolling
drift report from SQLite
2
Diagnose
Claude analyzes the
failure or opportunity
3
Propose ONE Action
Nav param tweak, harder
world, or mission plan
4
Human Approval
Nothing is applied
without a human "yes"
5
Apply + Re-test
Change lands, pipeline
runs again
Human-in-the-loop by design. Full unattended autonomy is roadmap, not a claim — under-claim, over-deliver.
Session 13 · tools/agentic_loop.py · built on the real drift detector, not hardcoded thresholds

## Slide 10
MULTI-SIM VALIDATION
Two Engines, One Test Suite
GAZEBO HARMONIC — Throughput Tier
• Fast, headless — seconds per full run
• CI-native, self-hosted RTX 5080 runner
• Nav2 + SMAC 2D planner, RPP controller
• Runs on every push (stage-3-gazebo)
ISAAC SIM — Fidelity Tier
• Photorealistic rendering, PhysX physics
• Perception-grade sensor simulation
• Same test file, same telemetry schema
• Runs on every push (stage-4-isaac)
Same tests/test_navigation.py, same telemetry_logger, same drift_config.yaml thresholds — different physics engine underneath.
autonomous-fleet-testbed

## Slide 11
MEASURED, NOT SIMULATED
Real Numbers From Real CI Runs
~1s
x86 native colcon build
(vs. 23+ min QEMU)
52s
Gazebo stage — cold start
through 3 nav tests
100s
Isaac Sim stage — cold start
through 3 nav tests
24m31s
arm64 image build
(QEMU cross-compile, x86)
From one real logged navigation run (Gazebo, Session 12):
• Position error: 0.15–0.18 m (within Nav2's 0.15 m goal tolerance)
• Odometry: 50.6 Hz · LiDAR: 10.4–10.6 Hz · Camera: 10.4–10.6 Hz
• Zero collisions · logged automatically to SQLite, validated by a Pandera schema gate
autonomous-fleet-testbed

## Slide 12
STACK
Built On
Robot Software
• ROS2 Jazzy
• Nav2 (SMAC 2D, RPP)
• CycloneDDS
Simulation
• Gazebo Harmonic
• Isaac Sim 6.0
• PhysX / OGRE2
CI/CD
• GitHub Actions
• Self-hosted RTX 5080 runner
• Docker Buildx + QEMU (arm64)
Telemetry & Data
• SQLite
• Pandera schema validation
• Streamlit + ReportLab
Intelligence Layer
• Claude API (Anthropic)
• Tool-use / structured diagnosis
• Human-in-the-loop approval
Target Hardware
• Jetson Orin Nano Super
• Waveshare UGV-PT
• ESP32 sub-controller
autonomous-fleet-testbed

## Slide 13
PROGRESS
13 Sessions Complete, 3 to Real Hardware
01–05
Foundation
Ubuntu, ROS2, Docker, GitHub repo, file migration
06–08
CI Gates
Requirements traceability, code quality, arm64 cross-compile
09–10
First Nav Test
URDF + Gazebo + Nav2, first green nav test, self-hosted runner
11–12
Fidelity + Telemetry
Isaac Sim integration, full telemetry → dashboard → drift pipeline
13
Agentic Loop
Claude diagnoses failures, proposes fixes, human approves
14–16+
Real Hardware
Jetson flash, real robot deploy, sim-to-real correlation, r1-complete

## Slide 14
ROADMAP
What's Next
R4 — NEXT (the differentiator)
• Closed-loop agentic test/heal on named failure modes — already scaffolded in Session 13
• Automated sim-to-real alignment auto-tune domain randomization so sim tracks reality
• Generative scenarios → real SDF natural-language prompt → an actual Gazebo world, not just JSON
R2 / R3 — optional demo flourish
• Multi-robot fleet coordination
• Drone added — aerial + ground coordination
• Fully autonomous, AI-defined missions
Pulled forward only if a specific role/customer/demo needs it.
The differentiator lives on the infrastructure axis — not the robot-count axis.
autonomous-fleet-testbed

## Slide 15
A disciplined, AI-augmented CI/CD pipeline
for autonomous robots.
Proven end-to-end in simulation today. On real hardware next.
Private repository — code available on request
Mike